# Node Parameters
Index	Value	Description
0	20	Number of supported parameters (not including itself)
1	13	Manufacturer Id
2	‘a’	Minor code version
3	82	Module Id
4	64	Number of supported events
5	5	Number of event variables
6	4	Number of Node variables
7	1	Major code version
8	119	Node flags 1 + 2 + 4 + 8 = 15 / 1: Consumer / 2: Producer / 4: FLiM / 8: Supports Bootloading / 16: Can consume own events / 32: In learn mode
9	3	CPU type the firmware is built for – P18F2480 / see the CBUS header files for a full list of codes
10	1	Transport type: / 1 – CAN / 2 – Ethernet / 3 – MiWi (Microchip mesh network)
11	0x00	Code load address (4 bytes to allow for future use of 32 bit processors) / 0x00000800
12	0x00
13	0x00
14	0x00
15	‘3’	CPU manufacturers code as read directly from the chip by the firmware (4 bytes) / 0x00001AE4
16	‘2’
17	‘8’
18	‘P’
19	2	Code for CPU manufacturer - CPUM_MICROCHIP
20	0	Beta release build number – set to zero for release version

# Node Variables
Index	Description	Range
1	Switch1 type	0=None, 1=On/Off, 2=Only On, 3=Only Off, 4=Toggle
2	Switch2 type	“
3	Switch3 type	“
4	Switch4 type	“

# Event Variables
Index	Description	Range
1	Producer index	0-4
2	Effect for LED1	0-4
3	Effect for LED2	“
4	Effect for LED3	“
5	Effect for LED4	“

# Supported Opcodes
0D	QNN
10	RQNP
11	RQMN
42	SNN
50	RQNN
51	NNREL
52	NNACK
53	NNLRN
54	NNULN
55	NNCLR
56	NNEVN
57	NERD
58	RQEVN
59	WRACK
5C	BOOTM
5D	ENUM
6F	CMDERR
70	EVNLF
71	NVRD
72	NENRD
73	RQNPN
74	NUMEV
75	CANID
90	ACON
91	ACOF
92	AREQ
93	ARON
94	AROF
95	EVULN
96	NVSET
97	NVANS
98	ASON
99	ASOF
9A	ASRQ
9B	PARAN
9C	REVAL
9D	ARSON
9E	ARSOF
B2	REQEV
B5	NEVAL
B6	PNN
D2	EVLRN
D3	EVANS
E2	NAME
EF	PARAMS
F2	ENRSP
AND	VLCB-specific

MDF:
{
  "timestamp": "202411092105",
  "moduleName" : "CAN1IN1OUT",
  "nodeVariables": [
    {
      "type": "NodeVariableNumber",
      "nodeVariableIndex": 1,
      "displayTitle" : "Nothing"
    }
  ],
  "eventVariables":[
    {
      "type": "EventVariableSelect",
      "eventVariableIndex": 2,
      "displayTitle": "LED Control",
      "options": [
        {"label": "Normal", "value": 1},
        {"label": "Blink", "value": 2}
      ]
    }
  ]
}